# Normalization
Before reconstructing an image, we need a normalization image. This is constructed with a command like
$ zcat norm.elm2.gz | elm2todkfz -o - - | Norm_Total_Gen <crystal distance in mm> <pixel length> - <norm image prefix>

It will produce a file named <norm_image_prefix>_total

# Reconstruction
Images can be reconstructed with a command like
$ zcat phantom.elm2.gz | elm2todkfz -o - - | ClearPEM_LMRec -i - -n <image prefix> -d <distance> --pixel-lentgh <pixel length> -o <image prefix>

The “-” are there so the programs use stdin/stdout, pipelining the data.
More options can be added to elm2todkfz and ClearPEM_LMRec. See next pages.
# Arguments for elm2todkfz
elm2todkfz [options] <input1.elm2> <input2.elm2> ... <inputN.elm2>

<input.elm2>
This sets the input file name. Any number of files may be specificed. If it's "-" then it uses stdin as input. Default is none, which is not very usefull.

-o <output.lm>
This sets the output file name. If it's "-", then it uses stdout as output. Default is none, no output is written (not very useful in general).

--energy-low <energy in keV>
--energy-high <energy in keV>
These set the energy window, discarding all data outside the window. Default is 400-650 keV

--time-window <time window in ns>
This sets the coincidence time window, discarding all events outside the window. Default is 4 ns.

--random-file <filename>
    This outputs the random events to another file. Default is none, no random file is written.

--half-life <isotope half life in minutes>
Enables decay correction, by setting a isotope half-life time-window.

--initial-time <intial time for decay correction (unix epoch)
Overrides the initial time used for decay correction.
# Arguments for ClearPEM_LMRec
ClearPEM_LMrec [options]

-i <input.lm>
This sets the input file name. If it's "-" then it uses stdin as input. Required.

-o <filename>
This sets the output file name. If it's "-", then it uses stdout as output. Required.

-d <distance>
This sets the distance between crystals in mm. Required.

-n <norm prefix>
This sets the prefix of the normalization file to use (sans the _total). Required

--pixel-length <size>
Voxel size in mm.

--iterations <N>
Performs N iterations. Default is 8, for no special reason.

--save-iterations <N>
Save image at every N iterations. Set to 0 to save only the last iteration. Default: 0.

--osem <0|1>
1 enables OSEM reconstruction, with one subset per acquisition angle. 0 disables, turning it to MLEM. Default is to use OSEM.

--no-interfile
Writes a “raw” image. Default is to write an Interfile image.

--filter-iter <N>
Applies the Metz filter every N iterations. 0 disables filtering. Default is 2.
--filter-fwhm <fwhm in mm>
Sets the filter's FWHM. 0 disables filtering. Default is 1.5 mm.
--filter-power <power>
Sets the filter's Metz power. 0 degenerates to a pure gaussian filter. Default is 0.

--partial <fraction in %>
Uses only a fraction of the events to reconstruct an image. Default is to use 100% of the events.

--threads <n>
Runs reconstruction with N threads. Default is 8.
--rays <n>
When N is 0 (default), each event is traced once using center crystals X-Y coordinates. When N is larger than 0, each event is traced N times, each time with a random ±1 mm shift in X-Y.

--rand-image <random file>
This option enables random correction based on the random image generated by Random_Gen

--rand-cut <random cut value C, 0 to 0.5>
When C is 0 (default), all the events will be considered for reconstruction. When C>0, then only the events with R < C will be considered for reconstruction, in which R refers to the possibility that this event is not a random coincidence. Setting C to 0.5 will have an “over-correction” effect.
# Arguments for Norm_Total_Gen
--threads <n>
Runs reconstruction with N threads. Default is 8.
--rays <n>
When N is 0 (default), each event is traced once using center crystals X-Y coordinates. When N is larger than 0, each event is traced N times, each time with a random ±1 mm shift in X-Y.

# Arguments for Random_Gen
Random_Gen [options] <plates distance> <pixel length> <norm prefix> <input file> <output file>

<input file>
This sets the input file name. The input file should be delayed coincidences generated from elm2dkfz with option --random-file.